TABLE OF CONTENTS

Section	 	Page

SAFETY INSTRUCTIONS: 		2

INTRODUCTION

Machine Specifications		3

Functions, Tooling, Drive		3 & 4

Picture of Heavy Duty Portable Mill		4

Illustration of Heavy Duty Portable Mill 		5

MACHINE SET-UP

Assembly Procedure		6

Installing Motor		6 & 7

Hydraulic Power Set Up	7

MACHINE OPERATION

Hole Drilling, Boring, and Chamfering		8

Resurfacing and Milling		9

Machine Maintenance, Record of Use		10

APPENDIX: PARTS/DIAGRAMS

Heavy Duty Portable Mill	11

Servo Drive		12

Heavy Duty Portable Mill Quill Housing		13

SAFETY INSTRUCTIONS

- Wear protective clothing, including safety glasses and steel toe boots.

- DO NOT allow loose clothing or long hair near machine operations.

- Keep work site and machine clean.  Use brush to remove chips.  DO NOT use hands or air hose.

- Ensure adequate clearance around pipe before mounting milling machine.

- Support machining surface for total machine weight.

- DO NOT rush the job.  Read this manual and understand the operating procedure before attempting any cutting operation.  Call our toll free number (1-800-328-1488) if any problems arise.

- Before connecting the hoses to the machine, be sure the following components are tightly secured: slide, tool bits, motor mount, and vertical feed support angle bracket.

- Be sure the mill is completely secured to the work surface before starting the machine.

- During actual machine operation, DO NOT touch or rest your hand on or near any moving parts or sharp edges.

- Disconnect  air hose or hydraulic power source BEFORE dismounting lathe from pipe.

- NEVER MOVE MACHINE WHILE CONNECTED TO AIR OR HYDRAULIC SUPPLY.  ALWAYS turn off control valve and disconnect hoses BEFORE attempting to move the machine.

INTRODUCTION

General Description

Mactech Heavy Duty Portable Mills are designed to make on-site, close tolerance machining cost effective.  Our mills can be clamped, bolted, or magnetically attached directly onto the workpiece and mounted in any direction.  Infinitely variable power feed is available on the vertical feed slide assembly.

MACHINE SPECIFICATIONS

Capabilities & Functions

Capabilities

- Drilling

- Chamfering

- Boring

- Tapping

- Surface machining

Functions

Mactech Heavy Duty Portable Mill are used to perform gamma plug installation, stud removal, thermoweld installation, and numerous other milling jobs.

The milling machine can machine steel and various alloys, stainless steel, aluminum, copper-nickel, nickel-copper-iron, and bronze.

Tooling

High speed tool steel bits, drill bits and milling bits or different sizes are available for most machining operations.  Mactech stocks many standard tool bit configurations.

Frame Components

The milling head assembly feeds vertically along the cast iron feed support angle bracket into the work piece. The vertical slide assembly is attached to X and Y travel slide  which enable for precise alignment or horizontal feed for surface machining. The side support rails only one setup.

Travel Slides

The slides are made of cast iron, comprised of ways and saddles with adjustable gibs, and full length feed screws.

Drive Assembly

- In-Line Air Drive (97 RPM max), also includes air caddy.

- Hydraulic drive (137 RPM max).

MACHINE SET-UP

Read SAFETY INSTRUCTIONS on page.

Assembly Procedure

Clear worksite of all obstructions and clean area.

Assemble aluminum base components (if needed) and install on working surface (see below).

Installation on Curved Surface (In-Line Pipe):

- Attach aluminum saddle to steel base by wrapping chains around pipe.

Note:  Have partner hold base while connecting chains around pipe.

- Square and level base to pipe surface (if necessary).

Attach cast iron vertical support bracket and slide to the steel base.

Square and level base (if necessary).

Installation on Flat Surface:

- Attach vertical support bracket to steel base and/or flat surface (bolt, tack weld, clamp, or magnetically attach).

- Square and level base.

Installing Motor

CAUTION!  Control Valve must be turned OFF before installation of motor.

- Insert motor so that keyed shaft aligns with the quill keyway.  Tighten motor mount screws.

- With control valve off, connect hoses to power supply/air supply.  Test run motor to check speed.

# Text boxes

MACTECH 48” HEAVY DUTY

PORTABLE MILL

OPERATING MANUAL

& PARTS LIST

SERIAL NO. ____________